## Slide 1: Switch led summary
Fanfan Liu
2014/05/27

## Slide 2: Topic
Part1: CLIs
Part2: automation command
Part3: automation script enhancement needed

## Slide 3: Part1
Part1: CLIs
<1> check switch power status
#show system power status
<2> check switch power color
#show system led
<3> change port mode to link/speed/duplex/poe
#_led button press link
#_led button press speed
#_led button press duplex
#_led button press poe

## Slide 4: Part1
<4> check the current port mode
#_hw i2c chan 0 chip 7f addr 13 width 1
AH-4295c0#_led button press link
AH-4295c0#_hw i2c chan 0 chip 7f addr 13 width 1 00000013: 70 p AH-4295c0#_led button press speed AH-4295c0#_hw i2c chan 0 chip 7f addr 13 width 1 00000013: b0 . AH-4295c0#_led button press duplex AH-4295c0#_hw i2c chan 0 chip 7f addr 13 width 1 00000013: d0 . AH-4295c0#_led button press poe AH-4295c0#_hw i2c chan 0 chip 7f addr 13 width 1 00000013: e0 .

## Slide 5: Part1
<5> check phy interface color
#_sh switch phy 0x1 0x3 0x10
Eth port 00000001, page 00000003, reg 00000010: 00008188
Field you may interested may be below:
0x1 : eth port number,hex 1~24(interface eth1/10==0xa here)
00008188 : phy reg value.
Register value & led status map:
0x8188 --> Link traffic: green blink ; no traffic: off;
0x8988 -- green(forced)
0x8889 -- amber(forced)
0x8088 -- green
0x8880 -- amber
0x888B -- amber blink
0x8080 -- green blink
0x8888 -- off .

## Slide 6: Part1
link mode:
<ffliu: interface has traffic pass, color : green blink>
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 00008188
<ffliu: shutdown interface or plug out line, color: off>
AH-4295c0#in eth1/10 shu
AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008888
AH-4295c0#no in eth1/10 shu AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008188

## Slide 7: Part1
speed mode：
<ffliu: interface speed 1000, color: Green>
AH-4295c0#in eth1/10 speed 1000
AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008088
<ffliu: interface speed 100, color: Amber> AH-4295c0#in eth1/10 speed 100 AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008880
<ffliu: interface speed 10, color: Amber> AH-4295c0#in eth1/10 speed 10 AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008080
<ffliu: shutdown interface , color: off>
AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008888

## Slide 8: Part1
duplex mode：
<ffliu: must turn off speed auto-neg first if you wanna set duplex mode to half/full>
AH-4295c0#in eth1/10 duplex half Error: Please turn off speed auto-neg first. ERROR: Invalid parameter(s)
<ffliu: not support duplex half under 1000 speed> AH-4295c0#in eth1/10 speed 1000 AH-4295c0#in eth1/10 duplex half Error: Not support duplex: half, check speed configure. ERROR: Invalid parameter(s) AH-4295c0#in eth1/10 speed 100 AH-4295c0#in eth1/10 duplex half
<ffliu: no matter speed, duplex full, color: green> AH-4295c0#in eth1/10 duplex full AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008088
<ffliu: no matter speed, duplex half, color: amber> AH-4295c0#in eth1/10 duplex half <ffliu: amber> AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008880 AH-4295c0#

## Slide 9: Part1
poe mode：
<ffliu: sw supply 802.3at power, color: amber>
AH-4295c0#show in eth1/10 pse Port ------------------------------------------------------------- Port name eth1/10 PSE status delivering Power mode 802.3at Power limit(W) 32.000 PSE priority low Port current(mA) 152.500 Port voltage(V) 57.035 Real consumption(W) 8.200 Port class Class 4 Power allocated(W) 8.200 Profile name 802.3at ------------------------------------------------------------- AH-4295c0# AH-4295c0# AH-4295c0#_sh switch phy 0xa 0x3 0x10 Eth port 0000000a, page 00000003, reg 00000010: 00008889

## Slide 10: Part1
poe mode：
<ffliu: sw supply 802.3af power, color: green>
AH-4295c0#show in eth1/10 pse
Port
-------------------------------------------------------------
Port name eth1/10
PSE status delivering
Power mode 802.3af
Power limit(W) 15.400
PSE priority low
Port current(mA) 157.685
Port voltage(V) 56.974
Real consumption(W) 8.200
Port class Class 4
Power allocated(W) 8.200
Profile name 802.3af
-------------------------------------------------------------
AH-4295c0#
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 00008988

## Slide 11: Part1
poe mode：
<ffliu: shutdown interface pse, color: off>
AH-4295c0#in eth1/10 pse shu
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 00008888
AH-4295c0#no in eth1/10 pse shu
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 00008988
<ffliu: disable sw pse founction, color: off>
AH-4295c0#no pse en
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 00008888
AH-4295c0#pse en
ERROR: cli ui wait reply timeout, input cmd: pse en, line 1586.
AH-4295c0#pse en
current pse is already enabled.
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 00008988

## Slide 12: Part1
poe mode：
<ffliu: eth1/5 connect pc that doesn't need switch to supply power, color: off>
AH-4295c0#_sh switch phy 0x5 0x3 0x10
Eth port 00000005, page 00000003, reg 00000010: 00008888
<ffliu: POE-PSE fault, trigger it manually, connect AP with 12V DC power first, then connect switch, color: off>
AH-4295c0#
AH-4295c0#_sh switch phy 0xa 0x3 0x10
Eth port 0000000a, page 00000003, reg 00000010: 0000888b

## Slide 13: Part2
basic automation commands
switch led testcase

## Slide 14: Part3
case: SW_system_led_3
<1>result: RPS part doesn't check
reason: testbed hasn't completed
<2>result: simulate plug out the RPS cable
reason: have no idea
case: SW_port_led_1
<1>result: simulate "stop port traffic" and "plug out line“ (step7-8)
reason: have no idea
case: SW_port_led_4
<1>result: cannot change the power mode (step02-13)
reason: testbed doesn't have PD need switch to supply power
<2>result: cannot trigger poe-pse fault condition(step16)
reason: testbed doesn't have PD need switch to supply power
have no idea how to trigger it.
Other cases compeleted.

## Slide 15: end
Q&A